COMPUTER ROOM AC UNITS

## CLOSE CONTROL EC PLUG FAN RANGE

- The close control EC plug fan range has 8 unit sizes providing nominal capacities of 20 - 140kW.

- Units are available in air cooled, chilled water and dual chilled water versions.

- Units are available in upflow, downflow and downflow front discharge displacement airflow configurations.

- Standard DX units on R410A with an option on R407C.

- Condensers can be selected for 30, 35, 40, 45 & 50 ambients.

- Standard units have backward curved direct drive EC fans.

- BMS interfaces available are MODBUS, BACnet MSTP, BACnet IP, SNMP IP, LON & Trend.

- Full range of options available including:

  - Reheat of various types

  - Humidifiers

  - Electronic expansion valves

  - Discharge and acoustic plenums

  - Floorstands and dampers

  - Upgraded filter class

  - Fire and smoke detectors

  - Water detection

  - Condensate pumps

| Model |  | 060 | 080 | 120 | 160 | 200 | 240 | 280 | 320 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Air Volume | m3/hr | 6230 | 8610 | 13660 | 18510 | 23360 | 28310 | 33360 | 38410 |
| Total Capacity - DX | kW | 18.3 | 27.5 | 46.8 | 62.0 | 82.0 | 105.0 | 124.0 | N/A |
| Sensible Capacity - DX | kW | 16.5 | 25.1 | 43.6 | 58.4 | 75.5 | 96.5 | 114.3 | N/A |
| Total Capacity - CW | kW | 20.2 | 28.5 | 46.8 | 63.9 | 83.0 | 97.9 | 117.8 | 137.8 |
| Sensible Capacity - CW | kW | 20.2 | 28.5 | 46.8 | 63.9 | 83.0 | 97.9 | 117.8 | 137.8 |
| Unit Length - DX | mm | 650 | 850 | 1650 | 2050 | 2450 | 2850 | 3250 | N/A |
| Unit Length - CW | mm | 650 | 850 | 1250 | 1650 | 2050 | 2450 | 2850 | 3250 |

- Capacity based on 22°C & 50%RH return air, and for chilled water, an entering temperature of 6°C.

- Unit measurements for depth and height are 850mm and 1980mm respectively, except for the 060 model which is 650mm in depth.